## Slide 1: Architectures & Performance

## Slide 2: Outline
Architectural Approaches
Processor Architectures
Current Trends

## Slide 3: Architectures & Parallelism
A long history – starts in the 50’s
Approaches tried
  Implicit parallelism – CPU Pipelining
  Vector Processors
  SIMD Machines
  “Regular Architectures”
  Shared Memory - UMA
  Shared Memory - NUMA
  Clusters

## Slide 4: 1) Implicit parallelism – CPU Pipelining
Assembly line parallelism
What do you do on branch?
All modern CPUs are pipelined

## Slide 5: 2) Vector Processors
Supercomputers (Cray)
High-level operations on vectors (50-100)
Scientific computations of matrices
Unwinding loops
Compiler driven

## Slide 6: 3) SIMD Machines
Single Instruction, Multiple Data (SIMD)
One control unit
Single “heart beat”
Many PEs
Thinking Machine’s CM2 – 64K single bit processors

## Slide 7: 4) “Regular” Architectures
Fixed interconnection topology
Distance = # of hops
Ring, tree, mesh, hypercube, etc
Network topology maybe explicit or implicit in programming model
CM5, IBM SP2, Cray T3E, …

## Slide 8: 5) Shared Memory - UMA
SMP – Symmetric Multi Processor
Great programming model
Hard to build, very hard to scale beyond 16-24 processors!
Snoopy caching schemes – listen to the bus!

## Slide 9: 6) Shared Memory NUMA
Non-Uniform Memory Access
A bunch of connected SMPs with hardware supported distributed caches
Much more scalable!

## Slide 10: 7) Clusters
Distributed Memory
Typical commodity multiprocessors/Networks
Beowulf
Message passing

## Slide 11: 8) Clouds

## Slide 12: Outline
Architectural Approaches
Processor Architectures
Current Trends

## Slide 20: SUN UltraSPARC T1/T2
8 cores
4/8 hardware supported threads per core
32/64 hardware supported threads

## Slide 21: SUN UltraSPARC T1/T2

## Slide 23: Intel: “Haswell-EP” (22 nm) Efficient Performance
Xeon as of 2015
Xeon E5-16xx v3 (uniprocessor): Cores 4-14
Xeon E5-26xx v3 (dual-processor): Cores 4-18
Xeon E5-46xx v3 (quad-processor): Core 6-18

## Slide 24: Intel: Tick-Tock
Processor development model adopted in 2007
Repeat
  Tick: Shrink die
  Tock: New Microarchitecture
History: See Wikipedia

## Slide 25: Outline
Architectural Approaches
Processor Architectures
Current Trends

## Slide 26: Clusters
Convergence towards generic parallel machine
Node = one or more procs., memory, Network assist.
Network = commodity, scalable, topology independent
Ride the technology curve!
But add accelerators at the node level

## Slide 27: Evolving Programming Models
Multicore
  Directives (eg OpenMP)
  Mixed models (eg. Cilk)
  Libraries (eg. Intel TBB)
Cluster – Message passing (eg. MPI)
GPUs – CUDA, OpenCL, OpenACC
Clouds – Message queues (eg. ZeroMQ)
Big Data Clusters - Map/Reduce & Hadoop

## Slide 28: Accelerators
GPU
Thousands of simple cores
Mixed SIMD/MIMD
4 types of memory
Custom code
Intel Phi
10’s of simple cores
MIMD
4 types of memory
Same code recompiled

## Slide 29: IBM Cell processor

## Slide 30: IBM Cell processor

## Slide 32: FLOPS – Floating Point Operations Per Second
Name | FLOPS | When
yottaFLOPS | 1024 | 
zettaFLOPS | 1021 | 
exaFLOPS | 1018 | 2020 ???
petaFLOPS | 1015 | Today for the biggest parallel machines
teraFLOPS | 1012 | Today for a single multicore or accelerator
gigaFLOPS | 109 | 
megaFLOPS | 106 | 
kiloFLOPS | 103 | 

## Slide 33: Rmax vs Rpeak
rank supercomputers based on their performance using the LINPACK Benchmark.
Rmax score = maximal achieved performance
Rpeak score = theoretical peak performance.
XSEDE system | Rmax | Rpeak
Stampede (TACC) | 5.17 petaFLOPS | 8.52 petaFLOPS
Kraken (NICS) | 961.9 teraFLOPS | 1.17 petaFLOPS
Keeneland (Georgia Tech) | 319.6 teraFLOPS | 614.5 teraFLOPS
Gordon (SDSC) | 285.8 teraFLOPS | 336.1 teraFLOPS
Lonestar (TACC) | 251.8 teraFLOPS | 301.8 teraFLOPS

## Slide 34: Peak Performance

## Slide 38: 500 Fastest Computers
Top 500: http://www.top500.org/
Breakdowns
  http://www.top500.org/statistics/list/
Poster : http://s.top500.org/static/lists/2013/06/TOP500_201306_Poster.pdf

## Slide 39: Exascale Computing Challenges
1000 x today’s petascale architectures
System power is the primary constraint.
  Target is 20-40 MW in 2020 for 1 exaflop
Clock frequencies likely decrease to conserve power
  Will likely need billion-way concurrency
Memory bandwidth and capacity not keeping pace flops.
  Current scaling approaches useless!
Exascale Report